## Slide 1: SIRDAS.Net
Introduction to SIRDAS.Net v3.11
February, 2024
Espen Halsaa Albrektsen espen@albrektsen.net
http://www.albrektsen.net/sirdas

## Slide 2: Agenda
Changes since v3.11
Getting started
  Installation
  What is SIRDAS.Net
Basic operation
  Opening a file
  Depth Reference measurements
  Snow Density measurements
  Data export
Advanced operation
  Manual route correction
  Data analysis tuning
    Vertical filters
    Horizontal filters
    Route finder

## Slide 3: Changes since v3.10
v3.11
  Exclude shots complete rewrite
  Possible to add position to marker if dataset is missing GPS
  Fixed “bug” in EvenSpacedDistanceFilter – “DistanceFromStart” is now always increasing

## Slide 4: Getting started
Download and install SIRDAS.Net from
  http://www.albrektsen.net/SIRDAS
  You need some Microsoft tools – these are downloaded automatically if not allready installed on your system
Start the application, and request a license key
  A request is posted to my web site – I manually generate a license key and email back to you. (Expect 1-3 bussiness days delay)
Start the application, and register the license key
Start the application – you are good to go! 

## Slide 5: Supported radar formats
NogginPlus (.dt1)
Malå (.rd3)
ImpulsRadar (.iprb)
For all data formats, there exists more than one file. SIRDAS assumes that files that belong together have the same filename. Typically
  A file with «markers»
  GPS data
  «metadata» - like radar serial number and settings

## Slide 6: Basic Operation
NogginPlus file format
  Each scan consists of 3 files, with file types ‘.dt1’, ‘.hd’ and ‘.gps’. These three files must be in the same directory and have the same filename:
  When a .dt1 file is selected for analysis, SIRDAS.Net immediately starts processing the file data.
  If the NogginPlus file contains reference points (Fiducial Markers in the NogginPlus manual). SIRDAS.Net assumes that a NogginPlus Fiducial Marker is a manual depth measurement, and allows the user to enter this information.

## Slide 7: Plot navigation
Mouse wheel is supported
  Rolling the wheel zooms in and out
  Wheel pans left and right (After you have zoomed)
Zoom out
  Press ESC key
  By using the mouse wheel
  By double clicking right mouse button
Zoom in
  By selecting a range
Pan
  By mouse or keyboard.
  Ctrl-arrow moves to start or end

## Slide 8: Depth References
Used to calibrate wave propagation velocity, and to to adjust for equipment-specific depth offset

## Slide 9: Purpose
Used to calibrate the conversion between sample index and depth.
  Average wave velocity defaults to 0.2m/ns
  The radar signal is sampled at a fixed interval (samplerate) – a sampleindex is therefore a representation of the two-way travel time from radar to ground and back
The wave velocity varies with snow density and needs to be calibrated
Zero-level
  Zero-level is initialized to the value calculated by the Cut-off-filter. (See filter section for details)
The zero-level offset depends on equipment and also needs to be calibrated.
Zero-level can be updated manually, or reference points for zero level can be entered.

## Slide 10: Depth Reference Form
ShotIndex is the position of this Depth reference
Depth is manually entered by the user
WaveVelocity for this shot
Average wave velocity
Two Way Travel Time for this entry

## Slide 11: Depth reference form
SIRDAS supports entering multiple depth measurements for each reference. The average value will be used:
The number of measures to enter can be configured:

## Slide 12: Depth Reference Form
Reference point is plotted at «correct» depth and position
Zero-level offset clearly visible in graph

## Slide 13: Zero-level index
Manual override either
  By entering a depth reference of zero meters
  Or by adjusting zero sample index directly

## Slide 14: Snow Density Observations
Used to calibrate the formula for converting snow depth to snow-water equivalent (SWE)

## Slide 15: Snow Density Measurements
Is used to calculate the snow-water –equivalent (SWE)
Since snow density is a function of several factors, many observations can be used to increase density prediction accuracy
The density equation is
where b is the Global Snow Density gradient

## Slide 16: Local vs Global Snow Density
Local Density
Global Density
Used to calculate the average density for this scan
Can be automatically selected if position data is registered in the snow density form
Used to calculate the global density gradient
Linear regression is performed to calculate b
Outliers can be automatically discarded

## Slide 17: Snow Densities
Exclude this observation by removing check mark
UTM position of this observation
Depth measured
Automatic outlier removal
Gross weight measured
Equipment used to take measure
Measured density
StdError of selected measures
R2 of selected measures
Global Density equation
Visualization

## Slide 18: SnowDensityForScanForm
Selected for local snow density
Distance from this observation to this scan
Resulting local snow density
Automatic selection (Requires position data)
Global snow density gradient, b
Local snow density equation

## Slide 19: Data Export
Saving data…

## Slide 20: Export Reports
Route data
  Detailed report (mostly for internal validation)
Snow Water Equivalent
  This is the «core» export from SIRDAS
Radar data
  Detailed report (mostly for internal validation)

## Slide 21: Snow Water Equivalent Report

## Slide 22: Export formats

## Slide 23: Report contents
Header

## Slide 24: Report contents
Report footer contains
  Depth References
  Snow Densities
  Density samplers
  Filter configuration

## Slide 25: Report contents - ctd
Report footer contains
  Radar information (From the radar header file)
  Snow Density Equation
  Filter configuration

## Slide 26: Saving data
The analysis can also be saved to a .SIRDAS file
  Contains all raw data used to generate the route
  Contains the image generated by the raw data (as a picture)
.SIRDAS files can be used
  To quickly review historic data
  To update SWE report data by modifying Depth Reference information or Snow Density Measures
In order to save disk space, SIRDAS files must be reprocessed before changing routes

## Slide 27: Historical data
SIRDAS also supports loading historical data onto the current chart
You can then select which files to import
  May need file upgrade because previous versions lacked information needed for the historical import
  You select a «root» folder, and SIRDAS will autoselect files that are «close» - GPS position data required

## Slide 28: Historical data
Files that are «close» are auto selected
Files saved in previous versions need upgrade

## Slide 29: Historical data
After the files are selected, they will show up as an overlay on the current year’s data.

## Slide 30: Advanced features
Manual route correction
Analysis configuration
Manual grouping
Excluding shots

## Slide 31: Manual Route override
Sometimes the SIRDAS analysis is unable to make a correct path through the data points.
You can then use the mouse the correct the data by drawing new datapoints
  Ctrl-mouse Adds «manual» points
  Ctrl-shift-mouse Removes route correction
Recalculate route to check effect

## Slide 32: Manual route correction
After correction:
After recalculation:

## Slide 33: SIRDAS Configuration
Filters, PeakDetectors and RouteFinders

## Slide 34: Overview
Vertical filters
  Focus on one radar shot
  Needed to suppress ringing and compensate for the attenuation of the radar signal through the snow
  Perform a «chain» of filters
Horizontal filters
  Uses GPS data to group shots that are geographically close
  SIRDAS-v3.9 also adds a «Manual Grouping Filter» that is useful if GPS data is missing/corrupt
Route finder
  the «core» of SIRDAS – finds the snow-ground reflection
Peak detector – more or less obsolete
Registration – license and your email in case of SIRDAS crash
GPS Config – GPS Options

## Slide 35: Filter configuration
Vertical filters
  NeighboringAverageRingingFilter
  DepthFilter – Compensates for signal attenuation in snow
  LowPassAndMagnitudeFilter – Removes high-frequency oscillations, and converts sample value to amplitude
Old and experimental filters
  CutOffFilter – Removes large signal at start of data
  FftRingingFilter
  GainBasedRingingFilterRingingFilter

## Slide 36: Why change filter config
It is very hard to accurately analyze the data at the «start» of the shot
  The outgoing signal amplitude is very large – sometimes even saturates the signal
  For small snow depths, the reflection signal is much weaker than the outgoing signal.
I call this effect «ringing» - and I have spent a lot of time trying to remove this artifact from the data
The best solution so far is to leverage the fact that the ringing is «constant» for a given file.
  Sometimes it is not – for example if something happens to the radar
  The «ringing» is not expected to be constant when snow depth is small

## Slide 37: Vertical filters
User interface for changing configuration
Shows preview of original data and filtered data
Available filters
Active filters (Drag and drop to change)
Preview filter effect
Which shot to preview
Modify filter parameters
Unfiltered
Filtered

## Slide 38: LowPassAndMagnitudeFilter
SmoothingFactor=0:
SmoothingFactor=1.3

## Slide 39: Neighboring Average Ringing filter
Cutoff sample
  All samples before cutoff are set to zero
  Reducing this number will increase processing time
  Setting it too large will lead to overestimating the snow depth
Last ringing sample
  This filter only applies to the start of the samples
  Increasing this will increase the processing time because more data must be processed
Neighbor mode
  Distance – when GPS available
  Shot index – when GPS missing
Max & Min distance:
  Shots that are within this selection for each shot is used to calculate the ringing

## Slide 40: CutOffFilter
Removes the large signal from the snow surface
Averages first n samples in all shots
Looks for first sample where average is below treshold:

## Slide 41: Depth filter
Compensates for the signal attenuation in snow:
b=0:
b=0.1:

## Slide 42: Horizontal filters
Combines shots that are «close» – requires GPS information to be present in radar data.

## Slide 43: Peak detector
Detects peaks in the filtered data – not really used anymore. (Version 3.0 used peaks, 3.1 has an improved route finder algorithm).

## Slide 44: Route finders
This is the core algorithm in SIRDAS.Net
  Version 3.1 introduced the «Advanced Cheapest Cost Route Finder»
  Uses DIJKSTRA algorithm to calculate the «cheapest» path through the radar data.
  Relies on a tunable cost function – this function makes it «expensive» for the route to make large jumps, and makes it «cheap» og through strong data points
  The parameters can be tuned – see tooltip for explanation.
The other route finders are less accurate, but are faster. They should be avoided, and are kept in the product primarily for historic reasons.

## Slide 45: Missing GPS data
- Sometimes, the GPS fails to deliver data
- How to recover the data anyway

## Slide 46: How to analyze data without GPS
Two options as of v3.11
  Manual grouping and update the TotalDistance property
  Add markers and set GPS position

## Slide 47: Manual Positions
If GPS data is missing – there is new menu
Pressing this menu will allow you to add positions for all markers

## Slide 48: Config change after adding pos
After adding manual positions, the filter may need to be updated
A GPS based horizontal filter should be added:
NB: There is a bug in 3.11.2 – after adding manual positions, manual groups are added. This will be fixed.

## Slide 49: Manual grouping
- This filter is designed to handle the scenario where the GPS data is missing

## Slide 50: Manual Grouping filter
After loading a file where GPS data is missing, right-click in order to get to the context menu:

## Slide 51: Validate the total distance

## Slide 52: Total distance can be changed

## Slide 53: Group all shots that were taken while not moving

## Slide 54: Editing manual groups
It is possible to modify manual groups
  Click a group, then drag the “corners” of the group marker:

## Slide 55: Delete a manual group
Use ctrl-shift+right click in order to delete a manual group:

## Slide 56: Analysis must be re-executed
You need to re-execute analysis after changing manual groups
  By default, this is done automatically
  However – if your file is very large, you may want to disable auto-analyze

## Slide 57: Exclude shots
It has been “possible” to exclude shots in SIRDAS.
  However – this has been buggy and the most frequent cause for fatal crashes.
In SIRDAS v3.11, the Exclude Shots feature was completely rewritten
  As a consequence, “old” files using excludes will need update on load
The new exclude feature is more focused

## Slide 58: Exclude shots use cases
The primary use case for excluding shots is the scenario where some obstacle forces you to take a detour that you want to exclude from the scan
This can now be done by right-clicking in the distance data while pressing ctrl key

## Slide 59: Exclude shot filter is auto-added

## Slide 60: Exclude section can be modified
Click the exclude group and drag the corners
Perform adjustments in the “Shot#” chart
Exclude groups can be dragged and deleted the same way manual groups can

## Slide 61: Options
Display options

## Slide 62: Options
Zoom Y-axis: Check this in order to zoom on the Y axis
Show Raw Data: Show the data without the horizontal positionfilter applied
Absolute sample coloring: When selected, the color showing the echo strength is scaled globally – default value is that each shot is scaled to maximize visibility. The relative sample coloring makes weak signals look strong – use absolute coloring when you suspect this…

## Slide 63: Plot navigation
Mouse wheel is supported
  Ctrl+wheel zooms in and out
  Wheel pans left and right (After you have zoomed)
Zoom out
  By using the mouse wheel
  By pressing the zoom out button:
Zoom in
  By selecting a range
Pan
  By mouse or keyboard.
  Ctrl-arrow moves to start or end